## Slide 1: Syrup dispenser
Project by Franziska Rothen & Meindi Zahiri

## Slide 2: features
inputs
Weighing scale to determine glass size & syrup/water level
Choice of syrup percentage via potentionmeter
End stop to home the platform
Motor to move the glass
Valves to fill the glass
LCD menu for navigation
outputs
Communication between the two µ-controllers via USART

## Slide 3: hardware
2 nucleo
1 mbed shield
2 electrovalves
Linear actuator (stepper motor)
Drv8825 driver
1kg load cell + Hx711 amplifier
Level shifter
2 relays
12V power supply
CO2 tank
Love

## Slide 4: Functionalities
SPI: LCD Screen
Timer: Debouncing
GPIO: Weighing scale
ADC: Potentiometer
USART: Communication

## Slide 5: Spi – lcd screen
LCD_Driver library
Navigation:
  Move forward in menu via button
Display prompts and results
General Info

## Slide 6: Spi – lcd screen
int step = 0;
if(button pressed)
step ++;
Pseudocode
if(step == 0)
menu1_display();
else if(step == 1){
menu2_display();
other_functionalities();
}
else if (step == 2)
…

## Slide 7: Timer – debouncing
Problem: skip step in menu
Solution:
  Timer in interrupt mode
TIM 1
  Internal clock
  Frequency = 20Hz
General Info

## Slide 8: Timer – debouncing
Pseudocode
bool button_state = true;
if(button pressed && button_state == true){
start timer;
button_state = false;
}
if(timer period elapsed){
if(button is reset){
step ++;
button_state = true;
stop timer;
}
}

## Slide 9: GPIO – weighing scale
24-Bit ADC: HX711
HX711 library
2 GPIO pins:
  DOUT (input)
  PD_SCK (output)
Calibration
Check weight for glass size
Check weight to stop syrup at percentage
General Info

## Slide 10: adc – potentiometer
ADC 1
  12-bit mode
  Scan conversion mode: enabeled
Values divided into 20 segments
5% up to 25% syrup (switch case)
General Info

## Slide 11: usart – communication
USART 1
  Asynchronous mode
Information to send:
  Open/close the valves
  Move the glass
General Info

## Slide 12: platform
Motor
  Stepper motor with stepper driver (2 pins)
Endstop
  Homing
  Safety
General Info

## Slide 13: Pneumatic
3/2 way electrovalve
  Bottles under pressure
Endstop
  Homing
  Safety
General Info

## Slide 14: Discussion
Valves operating pressure
Communication robustness (heartbeat, checksum)
Gpio reset state
Control for the flow
Scale readings could be improved
Menu improvement
General Info